## Slide 1: IS 380 Physical Security
Chapter 6

## Slide 2: Types of physical threats
Natural environmental threats
Supply system threats
Manmade threats
Politically motivated threats

## Slide 3: Life Safety
Protecting life is the first priority
Notes: P403

## Slide 4: . . Like an Onion
Layered Defense model
  If one layer fails, another layer protects.
Notes: P404

## Slide 5
Notes: P446

## Slide 6: CPTED
Crime Prevention Through Environmental Design – facility design, lighting and landscaping.
  Natural Access Control
  Natural Surveillance
  Natural territorial reinforcement
Target Hardening – locks, etc

## Slide 7: Physical Security
Deter
Delay
Detect
Assessment
Response

## Slide 8
Facility – location/terrain, proximity to fire/police, etc.
Construction
Entry Points
  Man trap
Fail safe
Fail secure
Notes: P422

## Slide 9: Water is not a datacenter’s friend
Internal partitions – do they go past the drop ceiling?
Windows – Standard, Tempered, Acrylic, Wired, Laminated, film (solar/Security)
Computer room location
  Access door (not doors).
  Emergency off switch
  Positive air pressure
  Fire suppression
Notes: P423

## Slide 10: HVAC
Dedicated HVAC system
  Temp 70°-74°F
  40%-60% humidity
Closed loop – air reused
Positive pressurization – smoke goes out
Store backups in a safe
  Encrypt backups

## Slide 11: Laptop safety
Inventory laptop, serial number. Engraving
Don’t let the laptop out of sight when traveling
Most laptop locks are a joke.
Back up your critical data.
Encrypt the hard drive (or at least critical data) – BitLocker – TruCrypt
Lojack for laptops.

## Slide 12: Clean Power
UPS
  Online - faster
  Standby – cheaper
  Voltage regulator/line conditioner
Spike/Surge, Fault/Blackout, Sag/brownout
In-rush current
Electromagnetic interference – other wires
Radio frequency interference – fluorescents
Generator
Notes: P432

## Slide 13: Fire: Prevent Detect & Suppress
Prevention – training, equipment, construction. BOXES
Detection – pull boxes, detectors, autodial
Suppression
Plenum area & plenum materials

## Slide 14: Fire Suppression
A – wood & paper - Water & foam
B – petroleum, natural gas – Gas, foam, powder
C – electrical – Gas, dry powders
D – metal – Powder/chemical specifically for Class D (NaCl, graphite, powdered copper)
K – cooking oil or fat (sub-type of class B)

## Slide 15: CO2, Halon, FM-200
Halon – CFC, 10% concentration danger
FM-200 - in

## Slide 16: Wet pipe/dry pipe
Wet pipe – always has water. Freezing problem.
Dry pipe – pipes dry until there is a fire
Preaction – dry pipe and thermal-fusible sprinklers.
deluge

## Slide 19: Locks
Keep honest people honest.
UL rating is on delay time.
Test | Door Locks/Cylinders | Security Container Key Locks | Two-Key Locks
Picking | 10 | 30 | 45
Impressioning | 10 | 30 | 45
Forcing | 05 | 30 | 05
Drilling | 05 | 30 | n/a
Sawing | 05 | 30 | n/a
Prying | 05 | 30 | n/a
Pulling | 05 | 30 | n/a
Punching | 05 | 30 | n/a
Notes: REF: http://www.lockwiki.com/index.php/UL_437

## Slide 20: Locks (cont)
Lockpicking
Keybumping
Kicking in the door
  Reinforce deadbolt strikeplate;the ‘weakest link’
  Use screws at least 3” long (studs behind door frame).
  About $3-$5 on amazon.com
Notes: REF: amazon.com

## Slide 22
Notes: Halligan bar

## Slide 23: Security in general
32.00% Through unlocked window or door
26.64% Forced entry by impacts
24.02% Prying or jimmying
6.79% Use of pass key or picking the lock
5.10% Entry attempted, but failed
5.45% Other or unknown

## Slide 24: More on locks
Warded lock – some padlocks
Tumbler lock
  Pin – most common
  Wafer – no keybumping
  Lever tumbler
Combination locks
Cipher locks

## Slide 25: Access cards
Magnetic swipe cards
Proximity cards – not all cards are created equal.
PIN?
Piggybacking

## Slide 26: How to respond to a physical attack?
Deterrence – Fences, Gates, Guards
Delay – Barriers, man traps, locks
Detection – Motion detectors, cameras, smoke alarms
Response procedures – Fire evacuation plan, emergency phone numbers

## Slide 27: Site selection questions
Crime in area
Emergency services available
Markings and signs on building
Accessibility
Some of these may run counter to non-security goals

## Slide 28: External protection mechanisms
Fencing (3’-4’, 6’-7’, 8’) different mesh
Gates
Bollards
Lighting – (critical areas 8’ high two foot-candles)
  Continuous, controlled, standby & responsive.
Surveillance devices – DVR, motion triggered recording/alerting
Guards and dogs
CPTED

## Slide 29: Intrusion detection systems
Beams of light
Sound and vibrations
Motion
Microwave, ultrasonic, or electrostatic fields
Electrical circuit (electromechanical)
PIR – passive infrared
Acoustical –prone to false alarm (some glass breaks are good)

## Slide 30: Guards
Flexible, good response, deterrent
Costly, usual personnel issues.

## Slide 31: Auditing physical access
Date and time of access attempt
Where access was attempted (Entry point)
User ID when access was attempted
Failed attempts, especially off-hours

## Slide 32: Tests and drills
Test evacuation plan
Test other plans so people know what to do in a real emergency.