## Slide 1: Telecommunications and Network Security or wow, this is a long chapter
IS 380

## Slide 2: Telecommunications
The electrical transmission of data among systems.

## Slide 3: OSI v.s. TCP/IP

## Slide 4: Encapsulation
Notes: P487

## Slide 5: Application
Closest to end user
File transmissions, message exchange, etc.
SMTP, HTTP, FTP, SNMP, TFTP, Telnet
PDU - message
Notes: p489

## Slide 6: Presentation
Formats information so the computer (application) can understand it.
  TIFF/JPEG/BMP
  ASCII/EBCDIC
  MPEG/MIDI
Compression and encryption
Notes: P490

## Slide 7: Session
Establishing connections between applications
Maintaining & terminating connection
NFS, SQL, RPC, NetBIOS
Modes
  Simplex, half duplex, full-duplex
Notes: P491

## Slide 8: Transport
Communication between computers
End-to-end data transport
TCP, UDP, SSL*, TLS, SPX
Reliable/unreliable transport
PDU – segment or packet
Notes: p494

## Slide 9: Network
Addressing and routing
IP, ICMP, IGMP, RIP, OSPF, IPX
PDU - datagram

## Slide 10: Data Link
LAN/WAN
Token Ring, Ethernet, ATM, FDDI
LLC – Talks to network layer (802.2)
MAC – Talks to physical layer (802.3, 802.11, etc)
SLIP, PPP, L2TP, ARP, RARP
The ‘bits’
PDU - frame
Notes: FDDI = fiber distributed data interface

## Slide 11: Physical
Encodes bits into electrical signals
Synchronization, data rates, line noise, timing.
HSSI, X.21, EIT/TIA-232, EIA/TIA-449

## Slide 12
Notes: P499

## Slide 13: TCP/IP
IP – Provides addressing and routing, connectionless protocol
TCP – Connection oriented, requires a source and destination port
  Reliable.
  Lots of overhead (30%+)
UDP – Connectionless (src and dst ports)
  best effort
  Low overhead
Notes: P500

## Slide 14: TCP ‘3-way’ handshake
SYN
SYN/ACK
ACK
Notes: P504

## Slide 15: Ports & sockets
Ports up to 1023 are well known – they have de facto services that run on them
Application automatically connect to the expected port – i.e. Internet Explorer connects to port 80
Socket – source and destination address and ports.

## Slide 16: In Class Lab
Run netstat
What connections are currently open?
What options are available in netstat?
What protocols are being used?

## Slide 17: In Class Lab (Cont)
Run Wireshark
Log into webmail
Do a text string search

## Slide 18: IPv6 - IPng
Eliminates need for NAT, however NAT has reduced the need for IPv6
IPSEC built in
128 bit address
Notes: P509

## Slide 19: Analog and Digital
Analog - EM waves. Modulated – frequency/amplitude.
  Sign wave
Digital – electrical pulses.
  Square wave

## Slide 20: Synchronous & Asynchronous
Asynchronous – no synchronization
  Low BW
  Stop and start bits
  modems
Synchronous – continuous stream, timing
  High BW

## Slide 21: Baseband & Broadband
Baseband – entire medium – Ethernet
Broadband – divided into channels - CATV
Notes: P512

## Slide 22: LAN networking

## Slide 23: Network typology
Notes: P513

## Slide 24: PAN, LAN, CAN, MAN, WAN
PAN – Bluetooth, IrDA, Z-wave, ZigBee
LAN – shared medium, cabling, etc.
  Star, Ring, Bus, Tree, Mesh
  Ethernet – ‘chatty’ CSMA/CD
  Token Ring – token passing 4/16
CAN
MAN
  FDDI – counter-rotating ring
Notes: P517

## Slide 25: Cable types
Coax
  ThinNet – 10Base2
  ThickNet – 10Base5
Twisted-Pair
  Shielded twisted pair
  Unshielded twisted pair
    Cat3, Cat5, Cat6
Fiber-optic
  Single-mode & multimode
Notes: p524

## Slide 26: Problems with cabling
Noise
  Crosstalk
  EMI/RFI
Attenuation - The higher the frequency. . .
cable length
  UTP –100m or 300’, ThinNet 185m
Security (Fiber, coax, STP, UTP)
Fire Rating – PVC VS fluoropolymer

## Slide 27: Token ring
24-bit token
Data placed and removed from token by the same device.
Multiple tokens?
Notes: P530

## Slide 28: CSMA
CSMA/CD Carrier sense Multiple access with collision detection.
CSMA/CA Carrier sense Multiple access with collision detection (WiFi)
Carrier, Contention, Collision, Back-off algorithm.
Broadcast domain
Collision domain
Notes: P531

## Slide 29: IP protocols - security
ARP – spoofing
DHCP – rogue server
ICMP – ‘Loki’ – backdoor channel
DOS:
  SYN flood

## Slide 30: Routing protocols
AS - Autonomous System
Dynamic Routing protocol
  Distance vector - # of hops
    RIP, IGRP (5 criteria)
  Link state – hops, size, speed, delay, load, etc. Calculate a typology. ^CPU ^RAM
    OSPF
Static Routing protocol
Route flapping
BGP
Notes: P539

## Slide 31: Network devices

## Slide 32: Network Devices
Repeaters – L1
  hub
Bridges – L2
  STA/STP
  Switches ‘multiport bridge’

## Slide 33: Network Hardware - Switches
Creates a private link between the destination and source
Prevents network sniffing
Allows for the creations of VLANS – physical proximity not required
VLANS allow greater resource control
  L3/L4 Switches – application specific integrated circuit. Tagging/MPLS/QoS

## Slide 34: Network hardware - Routers
Layer 3
Connect 2 or more networks
Traffic flow can be controlled by protocol, source address, destination address, or port number
Forwards broadcast data to an entire network

## Slide 35: Network Hardware - Gateways
Acts as a translator for unrelated environments
Can connect different protocols (IPX to TCP) or link technologies (Token Ring to Ethernet)
Most common example is a mail gateway that formats and forwards SMTP mail
Layer 7 (L3+)
  Network Access Server
PBX provides telephone switching

## Slide 36: Firewalls
Provide a “Choke point” in the network
Types:
  Packet Filtering
  Stateful inspection
  Proxy
  Dynamic packet filtering
  Kernel proxy
DMZ ‘firewall sandwich’ vs. Filtered Subnet
Notes: P554

## Slide 37: Firewalls – Packet Filtering
Based on a ruleset, or ACL – layer 3 info
Can access a limited amount of data about a packet (source, dest, protocol)
Not too smart = fast processing
Vulnerable to DoS attacks, spoofing, malicious data
1st generation Firewalls
Notes: P553

## Slide 38: Firewalls – Stateful inspection
Keeps track of connections in state table
Example – Will defend against a Syn flood
Allows for more complicated rules, such as only allowing responding traffic for a protocol
Require higher overhead – makes them vulnerable to DoS attacks
3rd generation
Notes: P556

## Slide 39: Firewalls - Proxy
Acts as the client for all connections
Outsiders only ever see the IP address for the firewall
Repackages all packets
May impact functionality in client-server model
2nd generation firewalls

## Slide 40: Proxy types
Application-Level – understand each protocol (Layer 7)
  less flexible
  more granular
  One proxy per protocol/Service
  Protect from spoofing, sophisticated attacks.
Circuit-Level – session layer. More flexible
  SOCKS

## Slide 41: Dynamic Packet Filtering FW
0-1023 well known ports
Allows to permit anything outbound and permit response only traffic.
  ACLs built as client establishes outbound connections
  UDP connections simply time out.
4th generation

## Slide 42: Kernel Proxy Firewall
Virtual network stack dynamically created for each packet
Inspection happens in kernel - fast
Packet scrutinized at all layers
Proxy-based system
5th generation Firewall
Notes: P563

## Slide 43: Firewall best practices
Block oddball ICMP (redirect, etc).
No source routing
Block directed broadcasts
Block ingress packets with internal or RFC1918 addresses. (spoofing)
Disable anything unused (default deny)
Look at logs.

## Slide 44: Firewall Architectures
Bastion Host – Directly connected to the Internet or DMZ, must be carefully hardened
Dual-Homed or Multi-Homed FW – Multiple NICs, connects internal and external networks
Screened host – router scans traffic before it goes to a firewall.
Screened Subnet – The area between the router and the first firewall, or the area between the firewalls. (I disagree)
Notes: P565

## Slide 45: DNS
Domain Name Service 1992 NSF; ‘hosts’
URL – Uniform Resource Locator
FQDN – Fully Qualified Domain name
Zones,
  Root, TLD – inverse tree.
  Authoritative server. Primary and 2ndary.
  Zone transfer
  Resource records
  Recursion

## Slide 46: DNS issues
DNS cache poisoning (race condition)
  No authentication
  DNSSEC and authentication (PKI). 2011
Hosts file and malware
Split DNS (corporate security)
Cyber squatters
Notes: P577

## Slide 47: Directory Services
Hierarchical database
  Classes, objects, schema, ACLs
Active Directory
Novell Directory Services
OpenLDAP
LDAP – Lightweight Directory Access Protocol

## Slide 48: NAT
RFC 1918 addresses
Short term fix to address depletion
Hides typology
Static mapping – one to one translation
Dynamic mapping – dynamic pool
PAT – many to one
Delayed the need for IPv6
Notes: P580

## Slide 49: Intranet/Extranet
Intranet
  Web-based application accessible from inside the company network
Extranets
  usually B2B
  EDI - Electronic Data Interchange
  Dedicated link?

## Slide 50: Local area networks in visio
In class lab

## Slide 51: Wide area networks

## Slide 52: MAN
Metropolitan Area Network
SONET – Synchronous Optical Network
  Redundant ring
  Local and regional rings
FDDI
Notes: p585

## Slide 53: WAN
MUX – multiplexing
SONET (US) & SDH (everyone else)
  Synchronous Digital Hierarchy
ATM – Asynchronous Transfer Mode
Dedicated Links / Leased Lines
Notes: p586

## Slide 54: WAN cont
CSU/DSU – Channel Service Unit/Data Service Unit
Circuit Switching – one set path. Voice.
Packet Switching – multiple possible paths
Frame Relay – shared bandwidth
  CIR – committed information rate
  PVC – guaranteed BW (CIR)
  SVC – teleconferencing, temporary remote site conn., voice calls.

## Slide 55: ATM
LAN, MAN, WAN
Cell switching
Connection oriented
53-byte cells

## Slide 56: QoS
ATM
  CBR – constant bit rate, voice/video -conn
  VBR – delay-insensitive – conn
  UBR – unspecified – no control of data rate. Connectionless
  ABR – available - guaranteed BW + leftover, conn
Notes: P599

## Slide 57: QoS non-ATM
Best-effort – actually the lowest QoS
Differentiated – middle-tier
Guaranteed service – High QoS: Voice/Video.

## Slide 58: Multiservice Access Technology
PSTN – public-switched telephone network
  SS7 Signaling System 7
  Circuit-based
VoIP – Voice over IP
  SIP
  Packet based
  Jitter
Notes: P602

## Slide 59: VoIP
H.323 – ITU-T standard – voice and video.
  Terminals, gateways, gatekeepers
VoATM, VoFR – connection-oriented, less jitter.

## Slide 60: VoIP - SIP
SIP – Session Initiation Protocol
  UAC – User Agent Client – soft phone
  UAS – User Agent Server – routing & signaling
  RTP – Real-time Transport – handle actual call
  Proxy – relay packets in network UAC & UAS
  Registrar – central record of everyone’s location on the local network.
  Redirect – keep identity while roaming (Enables intra-organizational routes)
Notes: P605

## Slide 61: SiP In Action

## Slide 62: SIP issues
Not encrypted
Interception and all other network security issues

## Slide 63: Remote Access
Notes: P610

## Slide 64: Dial-up and RAS
RAS server & RADIUS
PTSN network, Modem
Use of callbacks
Wardialing
56K
  MLPPP – >56k

## Slide 65: ISDN
Integrated Services Digital Network
Digital local loop
Point to point, on demand, fast call setup
BRI -Basic Rate Interface 2B 1D, 144Kbps
PRI -Primary Rate Interface 23B 1D 1.544Mbps (T1)
DDR Demand Dial Routing
  backup, expense, timeouts

## Slide 66: DSL
Digital Subscriber Line
2.5Mi from pop (18,000’)
52Mbps max
High and low frequency
SDSL – expensive, businesses
ADSL – what you use

## Slide 67: Cable Modems
50Mbps – shared
Requires ‘two way’ network
Reserved channels
DOCSYS
unencrypted

## Slide 68: VPN
Virtual Private Network
Private – encrypted. . . ?
3 kinds: IPSec, PPTP, L2TP
Remote users or remote networks
Encapsulation VS encryption
Notes: P615

## Slide 69: PPTP
Must be on IP network
PPP tunnel can contain other protocols
Optional encryption - MPPE

## Slide 70: L2TP
Works on more than IP networks
No encryption
  Use IPSEC (ESP) with L2TP
Supports RADIUS, TACACS+

## Slide 71: Authentication Protocols
PAP – Password Authentication Protocol
  Cleartext
CHAP – Challenge Handshake Authentication Protocol – encrypt string
  MS-CHAP, MS-CHAPv2
EAP – Extensible Authentication Protocol
  Framework for many kinds of authentication
  OTP, smart cards, biometrics, etc.
Notes: P621

## Slide 72: Remote Access Summary
Use a firewall – only allow necessary ports to remote users.
Split tunneling problem.
Security of ‘home’ computers
End users: look at SSL VPN instead of PPTP or L2TP.
Notes: P623

## Slide 73: Wireless Communications

## Slide 74: Wireless - A Few Details
Frequency vs. Amplitude
  Higher frequency: more data, shorter distance.
CSMA/CA – initial broadcast
Spread Spectrum – several frequencies at the same time.

## Slide 75: Spread Spectrum
FHSS – Frequency Hopping 802.11 (1-2M)
  Splits channel into Sub channels
  Hops between them ‘hop sequence’
  Reduces interference, can be fairly secure
DSSS – Direct Sequence 802.11b, GPS.
  Uses all available BW.
  Chips - Added pseudorandom noise at sub-bit level
  Looks like white noise
Notes: P625

## Slide 76: Spread Spectrum - Other(cont)
OFDM – Orthogonal Frequency-Division Multiplexing. 802.11a,g,n, ADSL, WiMAX
  Many slowly-modulated narrow narrowband signals perpendicular to each other.
  Low issues with multipath, attenuation
Notes: http://en.wikipedia.org/wiki/OFDM
http://www.iec.org/online/tutorials/ofdm/index.asp

## Slide 77: That whole 802.11 thing
802.11 – 1997 1-2Mbps 2.4GHz
802.11b – DSSS 11Mbps 2.4GHz
802.11a – OFDM 54Mbps 5GHz (h Europe)
  Shorter range, less crowded
802.11g – 54Mbps, 2.4GHz
802.11i – security, authentication

## Slide 78: Wireless (802.11b,g,a,n)
AP act as beacons
Modes
  Infrastructure – connected to LAN
  Stand-alone – wireless hub
  Ad hoc – no APs, P2P mode
Service Set ID (SSID)

## Slide 79: Wireless Authentication - old
OSA – Open system authentication (SSID)
  Clear-text communication
SKA – Shared Key Authentication
  WEP
    RC4 is symmetric – i.e. fixed shared key
    Initialization vector (IV) bad (reuse,↓ randomness)
    No packet integrity assurance – hackers can mess with ICVs making the integrity look ok
      (Integrity check value)

## Slide 80: Wireless Auditing tools
AirSnort
WepCrack
Aircrack-ng
coWPAtty
back|track

## Slide 81: Wireless Authentication - new
WEP is broken
  Temporal Key Integrity Protocol – some help with weak IV. Still RC4-based.
802.11i WPA, WPA2
  Use AES, not TKIP.
  EAP-TLS requires certificates
  Higher CPU, not backward compatible.

## Slide 82: 802.11i – AES
CCM Protocol (CCMP) – better encryption at lower layer
802.1X – port-based network access control. (L2)
  No network communication until authenticated.
  User authentication not system authentication
  With EAP - Mutual authentication possible
  Authentication server (RADIUS)
Notes: P633

## Slide 83: Wireless security
Use 802.11i/WPA2 enterprise (no PSK)
VPNs (put AP on DMZ)
Lower power/AP placement
MAC filtering
Test security

## Slide 84: 802.16 - WiMax
“last mile access”
Baltimore – Sprint, Clearwire (Xohm)
Compete with DSL/cable

## Slide 86: Cell phone security
Cloning
Cameras
Enterprise connectivity/data on phone
  APN
Security policies

## Slide 87: Malware
RootKits
Spyware/Adware
Email Spoofing
Instant messaging
  SPIM
  Corporate IM

## Slide 88: Other technologies to consider
IDS/IPS
Honeypots
SSL VPN
Notes: p582

## Slide 89: In Class Lab
Network diagrams with MS Visio